## Slide 1: DEAP 4.2 – Advisory Report 15th June 2021

## Slide 2: Advisory Report Trial
28 assessors participating
  Timelines
    December 2020 – AR builder enabled for participating assessors
    January 2021 – invited to provided feedback
    May 2021 – completion of further development on builder and on DEAP4/NAS integration
    8th June 2021 - launch of transitionary period and the updated advisory report tool for all domestic BER assessors
    6th July 2021 – Updated advisory report becomes official BER document and current advisory report retired

## Slide 3: Advisory Report Trial
Feedback
    Advisory report builder - UI, software application, recommendations etc
    Supports for assessors (technical document, BER leaflet for HOs, any additional supports?)
    Any homeowner feedback

## Slide 4: Generating official BER documents
    Send to NAS
    View survey in NAS
    Go through usual process to generate official BER documentation – BER cert and existing advisory report
    Issue official documentation to clients as usual

## Slide 5: Generating draft advisory report
    This step is optional for now.
    ‘Generate Advisory Report’ enabled when survey is sent to NAS
    New function generates the draft AR
    The draft AR will not appear in NAS until existing AR is retired
    Draft can be issued in addition to the official advisory report along with information leaflet for HOs explaining the trial
    After 6th July, there won’t be a ‘Generate Advisory Report’ button – it will be generated in the same manner as now

## Slide 6: DEAP 4.2 – Advisory Report

## Slide 7: Content
Overview
  Advisory Report Tool: a roadmap
  Logic & Approach
  Upgrade Measures & Recommendations
  Dependencies
  Minimum-Target Upgrade Level
  Worked Examples

## Slide 8: Introduction
Different audiences for the report
Address needs of different users

## Slide 9: Questions
We will try and answer as many as we can
Questions may be submitted to the Helpdesk
Generate an FAQ, or similar, to address all

## Slide 10: Overview

## Slide 11: Advisory Report tool: Roadmap
  Significant improvement on existing Advisory Report
  Help homeowner better understand energy performance of their home
  Build personalised package of upgrades to improve energy efficiency of their home
  Opportunity for assessors to sell their skills in a consultancy role

## Slide 12: Advisory Report tool: Roadmap
  Assessor builds a package of measures for that home to significantly improve BER
    Delivered in one project or over time (e.g. BRP)
  Colour coding to illustrate the current and potential energy performance
  Indicative level of investment for upgrades

## Slide 13: Logic & Approach
  Homeowners need guidance on where to start
  Fabric first, heating, renewables, other measures
  The full spectrum of upgrades is provided for
  Heat Loss Indicator (HLI)

## Slide 14: Upgrade Measures & Recommendations
  Suite of potential upgrades is based on existing performance
  Thresholds – these determine list of measures
  Upgrade values – the performance values of upgrades
  Automatic selection of measures
  Dependencies
    Heating fabric selected with notification
    Renewables fabric + heat pump selected with notification

## Slide 15: Threshold & Upgrade values - Fabric
Upgrade | Upgrade option available when | Upgrade Value
Wall | ˃0.44 | 0.35 / 0.27 / 0.18
 | ˃0.36 | 0.27 / 0.18
 | ˃0.27 | 0.18
Roof | ≥0.20 / 0.35 / 0.35 (ceiling / slope / flat) | 0.16 / 0.20 / 0.22
Windows | ˃1.49 | 1.4 / 0.8
 | ˃0.89 | 0.8
Doors | ≥2.7 | 1.4
Floors | ˃0.45 | 0.36 / 0.18 / 0.15
 | ˃0.27 | 
 |  | 0.18 / 0.15
 |  | 0.15
 | ˃0.24 | 

## Slide 16: Threshold & Upgrade values – Main Space Heating
Upgrade to | Upgrade when (system / efficiency) | Optimum
Heat Pump | Any, efficiency ≤ 100% | SH: 350%, DHW: 200% 1, 2
New boiler | Gas/oil boiler ≤ 86% Electric heating = 100% | Gas/oil boiler 90% efficient 3
Biomass boiler | Gas/oil boiler ≤ 77% Electric heating = 100% | Biomass boiler, 77% efficient 3
Electric heating | Electric heating | Electric heating 3
Solid fuel boiler | Solid fuel, ≤ 70% | Solid fuel boiler, 75% efficient
  HLI to be ≤ 2.3 – warning where this is not met
  If A2A, DHW is 100%
  Set to control category 3

## Slide 17: Optimal & Threshold values - Others
  Secondary heating: if ≤ 30% improve to 60% (solid fuel) / 90% gas heater, chimney -1, flue +1
  Renewable options presented if none in existing dwelling
  Mechanical ventilation (MVHR, MEV) if natural ventilation
  Simple measures, e.g., cylinder insulation/thermostat, draught stripping, draught seal of suspended timber floor all binary selections, e.g., if ‘Unsealed’ set to ‘Sealed’ etc.

## Slide 18: Measures & Dependencies
Assessor Selects | Automatically selected (if not already)
Floor insulation | Wall insulation, roof insulation, windows
Windows | Wall insulation, roof insulation
New boiler / biomass boiler | Wall insulation, roof insulation
Renewables | Wall insulation, roof insulation, windows, heat pump
Only selected Roof insulation upgrade and then selected Solar PV

## Slide 19: Minimum-Target Upgrades
Minimum: to allow publication
  Automatic selections will typically meet the minimum
Target: aligned with Climate Action Plan and Part L
Current | Minimum | Target
G | D2 | B2
F | D2 | B2
E2 | D1 | B2
E1 | C3 | B2
D2 | C2 | B2
D1 | C1 | B2
C3 | B3 | B2
C2 | B3 | B2
C1 | B2 | B2
B3 | B2 | B1
B2 | B2 | B1
B1 | B1 | A3
A3 | A3 | A2
A2 | A2 | A1
A1 | A1 | A1

## Slide 20: Notifications: Errors & Warnings
  Errors: Will prevent the publication of the Advisory Report
        The selected measures do not achieve the Minimum rating
        No additional measures selected (unless Minimum BER already achieved)
  Warnings: indicate that additional work may be required
        The selected measures do not achieve the Target rating
        The HLI is > 2.3 and a heat pump is selected

## Slide 21: Upgrade Builder

## Slide 22: Sample Upgrade Builder
Upgrade Builder
Dwelling Characteristics
Potential Measures
Potential Impacts
Reset selection

## Slide 23: Dwelling Characteristics

## Slide 24: Sample Upgrade Builder – Automatic Selections

## Slide 25: Sample Upgrade Builder – Additional Measures
  Symbol denotes additional measures
  Must select at least one (unless Minimum BER has already been achieved)

## Slide 26: Sample Upgrade Builder
Starting BER > Potential BER
Starting rating > Potential rating
Starting HLI > Potential HLI
Starting RER > Potential RER
Minimum BER / Target BER
Errors & Warnings
Level of investment cost

## Slide 27: Generating Advisory Report

## Slide 28: Sample Advisory Report
Page 1 – overview of the energy performance for the homeowner
Page 2 – Detail on the recommended measures
Page 3 – Technical detail
Page 4 – General information

## Slide 42: Worked Example
Starting rating: G

## Slide 44
  External Doors (1.4 W/m2K)
  Roof Insulation (0.16/0.20/0.22 W/m2K)
  Wall Insulation (0.35 W/m2K)
  Windows (1.4 W/m2K)
  Heat Pump options
  Lighting
  Draught stripping
  Cylinder Insulation

## Slide 45: Starting rating: G
Selected measures bring the rating from G to a B2
Selected measures bring the rating to 107.93 kWh/m2/yr
Selected measures bring the HLI to 1.851
Selected measures give an RER of 0.36
Meets Minimum upgrade rating (D2) and Target upgrade rating (B2)
Errors / Warnings
Indicative cost of implementing all selected measures

## Slide 47: Heat Pump & HLI

## Slide 48: Heat Pump & HLI

## Slide 49: Heat Pump & HLI
  Sometimes, HLI > 2.3 even with roof, walls, windows and floor upgrade
  Use DEAP to assess if there are areas within thresholds that may potentially warrant an upgrade
  However, a heat pump may not be a realistic option

## Slide 50: Generating Advisory Report

## Slide 55: Important
  Advisory Report is a starting point
  If working with a homeowner, will need to generate a more accurate picture of impact of measures in DEAP

## Slide 57: Further Worked Examples

## Slide 58: Starting rating: D2

## Slide 59: Starting rating: D2

## Slide 61
  External Doors
  Roof Insulation
  Wall Insulation (0.27 W/m2K)
  Windows (1.4 W/m2K)
  Heat Pump options
  Draught-seal suspended timber floor
  Lighting
  Draught Stripping
  Cylinder thermostat

## Slide 62
Selected measures bring the rating from D2 to a B2
Selected measures bring the rating to 107.48 kWh/m2/yr
Selected measures bring the HLI to 2.470
Selected measures give an RER of 0.39
2 notifications – 1 Warnings, 1 Error
Indicative level of investment to implement all selected measures
Achieved Minimum required BER and Target BER

## Slide 69: Starting rating: B2

## Slide 70: Starting rating: B2

## Slide 71: Starting rating: B2

## Slide 72: Starting rating: B2

## Slide 76: Starting rating: A2

## Slide 77: Starting rating: A2

## Slide 78: Starting rating: A2